## Slide 1
Methods for the Analysis and Modelling of Spatial Environmental Data
Wind Farm Suitability
Analysis
West of Hanover
Data Preparation · Georeferencing · Digitization
Nadia Farsiani
The Digital Landscape Model (Map 1) — the final deliverable

## Slide 2
The task, and my part in it
In an area of about 200 km² west of Hanover, suitable areas for wind turbines are to be identified from a Digital Landscape Model (DLM). My stage prepares the data the rest of the analysis is built on.
1
Setup & CRS
New project; 7 layers; EPSG:31467
2
Georeference
Aerial photo → map coordinates
3
Digitize
Trace the Leine oxbow arms
4
DLM map
Assemble & export Map 1

## Slide 3
1
STEP 1 OF 5
Project setup and coordinate system
Created a new QGIS project and loaded all seven shapefiles: study-area frame, roads, railways, power lines, water bodies, land use and places.
Checked the coordinate system: every layer is in EPSG:31467 (Gauss-Krüger zone 3) — a projected system measured in metres.
The project adopted this CRS from the data, so no reprojection was needed.
All distances (15–650 m) and areas are therefore measured in true metres directly.
EPSG:31467
projected coordinate system · unit = metre

## Slide 4
2
STEP 2 OF 5
Checking the data and its attributes
Opened the attribute table of each layer to find the fields the later analysis depends on.
Road class is stored in the field typ (Kreisstraße, Bundestraße, Landesstraße/Staatsstraße, Bundesautobahn).
Land use, water and railways are likewise classified in a typ field.
Key finding: the settlement types are held in the land-use layer — Ortslagen contains only place names.

## Slide 5
3
STEP 3 OF 5
Georeferencing the aerial photograph
The supplied aerial photograph had no spatial reference.
Placed ground control points by matching features in the photo (road junctions, water edges) to the vector layers.
Transformation: Polynomial 1 (affine), nearest-neighbour resampling, target EPSG:31467.
10 points placed; 1 outlier disabled, leaving 9 used for the fit.
5.1 px
mean error ≈ 20–25 m on the ground

## Slide 6
4
STEP 4 OF 5
Digitizing the oxbow arms of the Leine
The cut-off meander loops of the Leine are not in the water layer, so I traced them as new polygons. Result: 7 polygons in Altwasser.gpkg (field typ = 'Altwasser').
Aerial photograph — the oxbow arms are visible
Digitized result — 7 polygons over the aerial

## Slide 7
5
STEP 5 OF 5
Producing the Digital Landscape Model map
Assembled all data layers, the georeferenced aerial and the digitized oxbows in the QGIS print layout.
Styled the road network by class (the typ field).
Added the four required map elements: title, legend, scale bar and north arrow.
Exported the finished layout as DLM.pdf.

## Slide 8
Results & outputs
7
layers prepared
in EPSG:31467
5.1 px
georeferencing
mean error
7
oxbow polygons
digitized
Map 1
DLM map
produced
Files produced
final.qgz
the complete QGIS project
Luftbild_georef.tif
the georeferenced aerial photograph
Luftbild.points
the georeferencing control points
Altwasser.gpkg
the 7 digitized oxbow polygons
DLM.pdf
the exported Digital Landscape Model map
All files in one folder · relative paths · coordinate system EPSG:31467 throughout

## Slide 9
Methods for the Analysis and Modelling of Spatial Environmental Data
Buffer Analysis and
Exclusion Areas
West of Hanover
Safety Buffers · Settlement Classification · Total Exclusion Area
Khaled Alhamoud

## Slide 10
The task, and my part in it
Person 1 handed over the prepared DLM: seven layers, the georeferenced aerial photo, and the digitized oxbow arms. My stage turns every distance rule in the assignment into an actual exclusion layer — the mask Person 3 will subtract farmland from.
1
Check the data
one field, typ — and two compound values
2
Build 11 buffers
11 distance rules → 11 layers
3
Split settlements
spatial join solves a missing attribute
4
Combine
Merge → Fix → Dissolve → Clip
5
Check & hand over
Total_Exclusion_Area → Person 3
All eleven safety buffers, merged and colour-coded by class
96.4%
of the study area ends up excluded
11 → 1
buffers dissolved into one clean mask

## Slide 11
1
STEP 1 OF 5
Checking the data first
Every class I need — road type, land use, water, rail — lives in a single field: typ. Nothing is split across separate attributes.
Landnutzung.shp holds 2,919 polygons across 20 unique typ values. Ortslagen.shp, by contrast, carries only place names — no settlement-type field at all.
Key finding: some values are compound strings. The semicolon in 'Wald; Forst' and the comma in 'Landesstraße, Staatsstraße' are part of the value itself, not a separator between two classes.
That means every selection has to match the string verbatim — no LIKE wildcards, no splitting on punctuation, or the filter silently returns nothing.
typ
the one field every selection is built on
Select strings verbatim — no LIKE, no splitting.

## Slide 12
2
STEP 2 OF 5
Building the eleven safety buffers
Straßennetz.shp keeps every road class in one field (typ) — I only buffered the three categories the assignment names (Kreis-, Bundes-/Landes-, Bundesautobahn) and left Gemeindestraße and Weg untouched.
Distances range from 15 m for district roads up to 650 m for settlements — set with the Buffer tool, "dissolve result" switched on so same-class buffers merge automatically.
Same settings on every run for consistency: 16 segments per quarter-circle, round caps and joins.
Forest and oxbow arms (protected biotopes) both get a 200 m buffer; overhead power lines get 195 m — three times the 65 m rotor diameter.
All 11 buffers before merging
11 buffers
one per constraint class, 15 m to 650 m

## Slide 13
STEP 2 OF 5
Building the eleven safety buffers
All 11 buffers merged, before Total_Exclusion_Area is built

## Slide 14
3
STEP 3 OF 5
The settlement classification problem
The assignment splits settlements into two classes with different distances: settlements 'assigned to a local location' (650 m) and individual houses or splinters that are not (450 m).
Landnutzung.shp doesn't carry that distinction — every settlement patch is just typ = 'Siedlungsflaeche', with nothing to tell the two apart.
Solved it spatially instead of by attribute: any Siedlungsflaeche polygon touching a named village in Ortslagen counts as assigned (650 m); anything that doesn't touch one is a splinter (450 m).
Result: 1,640 of 1,771 settlement polygons (≈3,231 ha) sit inside a named village; 131 (≈118 ha) stand on their own.
1,640 / 131
settlement patches: assigned vs. splinter
650 / 450 m
buffer distance for each class
No attribute solved this — a spatial join with Ortslagen did.

## Slide 15
4
STEP 4 OF 5
Merging everything into one exclusion layer
1
Merge
all 11 buffer layers combined into a single layer
2
Fix geometries
cleaned up before dissolving, not after — repairing first keeps the topology clean going into the dissolve
3
Dissolve
no grouping field, so every touching buffer melts into one shape with no leftover internal lines
4
Clip
cut to the Frame boundary, so buffers sticking out past the study area don't count
Total_Exclusion_Area
One feature-a single MultiPolygon object

## Slide 16
Results & outputs
Being precise here mattered: the assignment's own '~200 km²' is a rough figure. The Frame boundary actually measures 181.78 km² — and that's the number the final percentage is built on.
181.78 km²
study area (Frame),
measured, not estimated
96.4%
of the area excluded
once every buffer applies
658 ha
left over — scattered
candidate patches for Person 3
1
final exclusion feature,
clipped to the Frame
Files produced
Total_Exclusion_Area.gpkg — final exclusion layer — main deliverable
Buffer.gpkg — all 11 buffers + merged/dissolved intermediates, kept for traceability
Altwasser.gpkg / Luftbild_georef.tif — carried over from Person 1
5
STEP 5 OF 5

## Slide 17
Key expressions & formulas
Copy-ready, and verified against the data before use
1 · Selection expressions
"typ" = 'Kreisstraße' → 15 m
"typ" IN ('Bundestraße','Landesstraße, Staatsstraße') → 20 m
"typ" = 'Bundesautobahn' → 40 m
"typ" = 'Wald; Forst' → 200 m
"typ" IN ('Indus.-Gew.-Fl.','Fl. fkt. Praeg.') → 650 m
"typ" = 'Siedlungsflaeche' → extract
2 · Spatial split (Extract by location)
Siedlungsflaeche ∩ Ortslagen (intersects) → 650 m
Siedlungsflaeche \ Ortslagen (disjoint) → 450 m
3 · Area & exclusion rate
A_ha = $area / 10000
P_ex = (17,519.48 / 18,177.8) × 100 ≈ 96.4%
4 · Tested, then removed — no effect
$area < 10,000,000
→ largest forest polygon: 261.8 ha
→ largest settlement polygon: 22.0 ha
→ both far below the threshold, so the filter excluded nothing
Verbatim strings only
no LIKE, no wildcards, no splitting on ';' or ','